PLDocument:  C:\MyFiles\Machxl50_\DDSCTRL\Ddspal00.doc
                  TITLE PAGE  Wed Aug 20 14:56:16 1997



     MACHXL - (c) Copyright MINC Incorporated 1987-1996


==============================================================================

     TITLE    : DDSPAL00.SRC
     FILE     : C:\MyFiles\Machxl50_\DDSCTRL\Ddspal00.mpf
     DATE     : Wed Aug 20 14:56:16 1997
     ENGINEER : Bill Sisk
     COMPANY  : Arecibo Observatory
     PROJECT  : DDS Controller IPack Board
     REVISION : 0

     COMMENTS : Using 22V10

==============================================================================


     MODULES  :

        Document Generator     	  3.66
        File Handler           	  5.2
        Language Compiler      	  3.79
        Architectural Optimizer	  3.92
        Device Lib Scan        	  3.108
        Device Library         	  3.201
        Device Partition       	  3.186
        Device Fusemap         	  3.85



     SWITCH VALUES :

        (Value in parenthesis represents batch mode switch value)

        PLCOMP PRODUCT TERM LIMIT : 128
        PLOPT  PRODUCT TERM LIMIT : 128
        PLOPT REDUCTION  :   Espresso (1)
        NODE GENERATION  :   Procedure Instantiation
                             Arithmetic and Relational Operators (1)



PLDocument:  C:\MyFiles\Machxl50_\DDSCTRL\Ddspal00.doc
                  EQUATIONS  Wed Aug 20 14:56:16 1997


EQUATIONS FOR SYSTEM

INPUT SIGNALS (9) :

       CLK
       LOW_TRUE   IOSEL
       LOW_TRUE   INTSEL
       LOW_TRUE   IDSEL
       RW
       LOW_TRUE   RES
       A1
       LOW_TRUE   INT0
       LOW_TRUE   INT1

OUTPUT SIGNALS (10) :

       WRT
       LOW_TRUE   RD
       LOW_TRUE   ACK
       OE
       D0
       LOW_TRUE   INTREQ1
       LOW_TRUE   INTREQ0
       NC[2..0]


REDUCED EQUATIONS:


WRT.D = IOSEL*/RW ;  "(1 term, 2 symbols)
WRT.CLK = CLK ;  "(1 term, 1 symbol)
WRT.RESET = RES ;  "(1 term, 1 symbol)

RD.D = IOSEL*RW ;  "(1 term, 2 symbols)
RD.CLK = CLK ;  "(1 term, 1 symbol)
RD.RESET = RES ;  "(1 term, 1 symbol)

ACK.D = IDSEL
                 + INTSEL
                 + IOSEL ;  "(3 terms, 3 symbols)
ACK.CLK = CLK ;  "(1 term, 1 symbol)
ACK.RESET = RES ;  "(1 term, 1 symbol)

OE.D = A1*INTSEL ;  "(1 term, 2 symbols)
OE.CLK = CLK ;  "(1 term, 1 symbol)
OE.RESET = RES ;  "(1 term, 1 symbol)

D0.EQN = 0 ;  "(1 term, 0 symbols)
D0.OE = OE ;  "(1 term, 1 symbol)

INTREQ1.EQN = INT1*/RES ;  "(1 term, 2 symbols)

INTREQ0.EQN = INT0*/RES ;  "(1 term, 2 symbols)

NC[2].EQN = 0 ;  "(1 term, 0 symbols)

NC[1].EQN = 0 ;  "(1 term, 0 symbols)

NC[0].EQN = 0 ;  "(1 term, 0 symbols)


PLDocument:  C:\MyFiles\Machxl50_\DDSCTRL\Ddspal00.doc
                  SOLUTIONS  Wed Aug 20 14:56:16 1997


 PARTITIONING CRITERIA : 


WEIGHT PRICE 10 ;

TEMPLATE = P22V10  ;






PARTITIONING SOLUTIONS : 

==> Solution  1: P22V10 



FUSEMAP FILES FOR SOLUTION 1: 

  Device 1 (P22V10) : C:\MyFiles\Machxl50_\DDSCTRL\Ddspal00.j1


PLDocument:  C:\MyFiles\Machxl50_\DDSCTRL\Ddspal00.doc
                  PINOUT DIAGRAMS  Wed Aug 20 14:56:16 1997


                              Device  1 - P22V10
                            --------\___/--------
                            |                   |
                    CLK  1 [| In/CLK        Vcc |] 24  
                            |                   |
                  IOSEL  2 [| Input       Biput |] 23 WRT
                            |                   |
                 INTSEL  3 [| Input       Biput |] 22 RD
                            |                   |
                  IDSEL  4 [| Input       Biput |] 21 OE
                            |                   |
                     RW  5 [| Input       Biput |] 20 D0
                            |                   |
                    RES  6 [| Input       Biput |] 19 ACK
                            |                   |
                     A1  7 [| Input       Biput |] 18 NC[0]
                            |                   |
                         8 [| Input       Biput |] 17 NC[1]
                            |                   |
                         9 [| Input       Biput |] 16 NC[2]
                            |                   |
                        10 [| Input       Biput |] 15 INTREQ0
                            |                   |
                   INT0 11 [| Input       Biput |] 14 INTREQ1
                            |                   |
                        12 [| GND         Input |] 13 INT1
                            |                   |
                            ----------------------
DEVICE SELECTION: 

         Device        Manuf   Fam    Pack   Temp   Price  User1 User2

==> PALCE22V10H-25PC/4  AMD    CMOS   DIP    COM    $  3.38    0    0
 2) PALCE22V10Q-25JC/4  AMD    CMOS   JLCC   COM    $  3.75    0    0
 3) PALCE22V10Q-25PC/4  AMD    CMOS   DIP    COM    $  3.75    0    0
 4) PALCE22V10H-25JC/4  AMD    CMOS   JLCC   COM    $  3.83    0    0
 5) PALCE22V10H-25SC/4  AMD    CMOS   FP     COM    $  3.83    0    0
 6) AMPAL22V10PC        AMD    TTL    DIP    COM    $  4.10    0    0
 7) AMPAL22V10JC        AMD    TTL    JLCC   COM    $  4.10    0    0
 8) AMPAL22V10AJC       AMD    TTL    JLCC   COM    $  4.35    0    0
 9) AMPAL22V10APC       AMD    TTL    DIP    COM    $  4.35    0    0
10) PALCE22V10H-15JC/4  AMD    CMOS   JLCC   COM    $  6.00    0    0
11) PALCE22V10H-15PC/4  AMD    CMOS   DIP    COM    $  6.00    0    0
12) PALCE22V10H-15SC/4  AMD    CMOS   FP     COM    $  6.00    0    0
13) PALCE22V10Q-15JC/5  AMD    CMOS   JLCC   COM    $  7.13    0    0
14) PALCE22V10Q-15PC/5  AMD    CMOS   DIP    COM    $  7.13    0    0
15) PALLV22V10Z-25JI    AMD    CMOS   JLCC   EXT    $  7.30    0    0
16) PALLV22V10Z-25PI    AMD    CMOS   DIP    EXT    $  7.30    0    0
17) PAL22V10-15PC       AMD    TTL    DIP    COM    $  7.50    0    0
18) PAL22V10-15JC       AMD    TTL    JLCC   COM    $  7.50    0    0
19) PALCE22V10Z-25JC    AMD    CMOS   JLCC   COM    $  8.16    0    0
20) PALCE22V10Z-25PC    AMD    CMOS   DIP    COM    $  8.16    0    0
21) PALCE22V10Z-25SC    AMD    CMOS   SOIC   COM    $  8.16    0    0

PLDocument:  C:\MyFiles\Machxl50_\DDSCTRL\Ddspal00.doc
                  WIRELIST  Wed Aug 20 14:56:17 1997

  +------------------+-------------------+-------+
  |      Signal      |       Device      |  Pin  |
  +------------------+-------------------+-------+
  | CLK              | P22V10_1          |    1  |
  | IOSEL            | P22V10_1          |    2  |
  | INTSEL           | P22V10_1          |    3  |
  | IDSEL            | P22V10_1          |    4  |
  | RW               | P22V10_1          |    5  |
  | RES              | P22V10_1          |    6  |
  | A1               | P22V10_1          |    7  |
  | INT0             | P22V10_1          |   11  |
  | INT1             | P22V10_1          |   13  |
  | WRT              | P22V10_1          |   23  |
  | RD               | P22V10_1          |   22  |
  | ACK              | P22V10_1          |   19  |
  | OE               | P22V10_1          |   21  |
  | D0               | P22V10_1          |   20  |
  | INTREQ1          | P22V10_1          |   14  |
  | INTREQ0          | P22V10_1          |   15  |
  | NC[2]            | P22V10_1          |   16  |
  | NC[1]            | P22V10_1          |   17  |
  | NC[0]            | P22V10_1          |   18  |
  +------------------+-------------------+-------+