ARECIBO OBSERVATORY

SERVO DRIVE SYSTEM UPGRADE




Programmable Logic Controller

Simatic S5 - 135U

LIST OF PLC ROUTINES

Software No. S1095034C-2.1

 


December 1999

Vertex Antennentechnik GmbH
Baumstr. 50
47198 Duisburg
Germany
Tel. +49-2066-2096-0; Fax -11

Contents

1. PROGRAM ORGANIZATION

1.1. Routine Types

1.2. Software Organization Overview

2.    LIST OF ROUTINES

2.1. Organization Blocks

2.2. Program Blocks

2.3. Function Blocks

2.4. Data Blocks

# 1.	Program Organization

## 1.1.	Routine Types

══════════════════════════════════════════════════════════════════

Organization	)

Time driven interrupts	)-- OB ...

Special functions	)

Subreflector control	PB ...; FB ...; FX ...

Data blocks	DB ...; DX ...

══════════════════════════════════════════════════════════════════

## 1.2.	Software Organization Overview

PB	FB, FX	DB

------------------------------------------------------------------

General functions	10- 49	180-255	10-49

supervisory functions	 10- 19

displays + control panels	 20- 29

------------------------------------------------------------------

positions 	50- 99	200-255	50- 99

------------------------------------------------------------------

operation	100-149	180-200	100-149

------------------------------------------------------------------

drives 	150-199	210-229	150-199

------------------------------------------------------------------

interfaces	220-255	230-239	220-255

------------------------------------------------------------------

library functions		1-179

------------------------------------------------------------------

# 2.   	List of Routines

## 2.1.	Organization Blocks

══════════════════════════════════════════════════════════════════

Program organization	OB 1

──────────────────────────────────────────────────────────────────

Interrupt routine

OB 2

──────────────────────────────────────────────────────────────────

Time driven interrupts	OB 10	called every 10 ms
		OB 11	called every 20 ms

OB 10... OB 18	OB 12	called every 50 ms

OB 13	called every 100ms

OB 16	called every 1 s

──────────────────────────────────────────────────────────────────

Special events	OB 20	cold restart

OB 21	manual warm restart

OB 20 ... OB 22	OB 22	power-up 
		OB 31	internal time out

──────────────────────────────────────────────────────────────────

Integrated special functions	OB 152	cycle time statistics
		OB 180	variable DB access

OB 182	copy DWs
		OB 190	transfer flags into DWs

OB 191	transfer DWs into flags

OB 220	sign extension 
		OB 221	set main loop timeout

──────────────────────────────────────────────────────────────────

## 2.2.	Program Blocks

══════════════════════════════════════════════════════════════════

General Functions

PB 10 ... PB 49

Supervisory functions	PB 10	control locations & general faults

PB 10 ...  PB 19     	PB 11	general functions

PB 15	emergency off

-------------------------------------------------------------

Displays and Panels

PB 20 ... PB 29	PB 21	Portable Control Unit

──────────────────────────────────────────────────────────────────

Positions

PB 50 ... PB 99

Position evaluation	PB 50	evaluation of positions (interrupt)

PB 50 ... PB 59	PB 51	read positions

PB 52	encoder selection & supervision

PB 53	limits

PB 54	encoder preset

──────────────────────────────────────────────────────────────────

Operation

PB 100 ... PB 149

General functions	PB 100	general functions during op.

PB 100 ...  PB 109     	PB 102	signals & horns
		PB 109	brake release supervision

-------------------------------------------------------------

Modes	PB 110	Program Track

PB 110 ... PB 119	PB 111	Stow

──────────────────────────────────────────────────────────────────

Program Blocks (cont'd)

══════════════════════════════════════════════════════════════════

Drives

PB 150 ... PB 199

Azimuth Drives 	PB 150	release / faults

PB 150 ... PB 159     	PB 151	drive functions

PB 152	switch off all drives

PB 153	local functions

PB 154	computer mode 
		PB 155	brakes

PB 156	cable car interlocks

-------------------------------------------------------------

Gregorian Dome	PB 160	release / faults

PB 160 ... PB 169     	PB 161	drive functions

PB 162	switch off all drives

PB 163	local functions

PB 164	computer mode 
		PB 165	brakes
		PB 166	regeneration failures

-------------------------------------------------------------

Carriage House	PB 170	release / faults

PB 170 ... PB 179     	PB 171	drive functions

PB 172	switch off all drives

PB 173	local functions

PB 174	computer mode 
		PB 175	brakes

──────────────────────────────────────────────────────────────────

Interfaces

PB 220 ... PB 239

CP 581	PB 220	interface to CP 581

PB 220 ... PB 229 	PB 221	transfer data to CP581 (interrupt)

PB 222	receive data from CP581 (interrupt)

PB 223	communication with CP581

──────────────────────────────────────────────────────────────────

## 2.3.	Function Blocks

══════════════════════════════════════════════════════════════════

Library functions

FB 1 ... FB 179

General functions	FB 50	intermittent light generator

FB 50 ... FB 59	FB 51	clear DB
		FB 52	copy DWs
		FB 59	idle block

-------------------------------------------------------------

Control functions	FB 61	parameters for setpoint limiter

FB 60 ... FB 99     	FB 62	PI controller

FB 64	loop reset

FB 66	setpoint limiter

FB 68	velocity ramp generator

-------------------------------------------------------------

Handling Blocks	FB 120	SEND

FB 120 ... FB 127	FB 121	RECEIVE

FB 123	CONTROL

FB 124	RESET

FB 125	SYNCHRON

FB 126	SEND-ALL

FB 127	RECEIVE-ALL

-------------------------------------------------------------

Encoder Evaluation Module	FB 130	initialization

FB 130 ... FB 137	FB 131	readout

FB 133	DB check

-------------------------------------------------------------

Communication

FB 160  ...   FB 179     	FB 173	checksum

──────────────────────────────────────────────────────────────────

Function Blocks (cont'd)

══════════════════════════════════════════════════════════════════

User Blocks

FB 180 ... FB 255, FX 0 ... FX 255

Operation	FB 180	Rate mode control loops

FB 180 ... FB 189	FB 181	Preset mode control lops

FB 182	Program Track control lops

FB 184	no operation control

FB 186	Program Track control

FB 187	Program Track start-up

-------------------------------------------------------------

Aux. arithmetic functions	FB 190	absolute difference
	FB 190 ... FB 199	FB 191	evaluate next stack data set
		FB 192	Program Track stack search

FB 193	potentiometer hysteresis

FB 194	Program Track ramp

FB 195	position increment calculation

FB 196	velocity feedforward

FB 198 	byte check
		FB 199	position limit check

-------------------------------------------------------------

Internal functions	FB 200	general functions

FB 200 ... FB 209	FB 201	lamp test

FB 207	cold restart  functions

FB 208	reset automatic functions

FB 209	start-up functions

-------------------------------------------------------------

Drive functions	FB 210	drive control

FB 210 ... FB 219	FB 211	prepare inputs for drive control

FX 210 ... FX 219	FB 212	Az bending

FB 213	gravity compensation

FB 214	torque bias

FB 215	drive to stow

FB 216	limits

FB 217	motor heating

FB 218	GD-CH interlock

FB 219	cable car interlock limits

-------------------------------------------------------------

Function Blocks (cont'd)

══════════════════════════════════════════════════════════════════

Aux. functions	FB 220	evaluate positions

FB 220 ... FB 229	FB 221	read positions

FB 222	cycle time measurement

FB 223	load loop parameters
		FB 224	CH gravity compensation in Aux
		FB 225	drive standstill after Preset

FB 226	encoder readout failure handling
		FB 227	auxiliary flags
		FB 229	time synchronization

-------------------------------------------------------------

Interfaces	FB 230	positions for CP581

FB 230 ... FB 239 	FB 231	evaluate data from CP581

FB 232	evaluate data from PCU

FB 233	prepare data for PCU

FB 234	axis related PCU data

FB 235	pepare data for SRC

FB 236	axis command evaluation

-------------------------------------------------------------

Monitoring functions	FB 250	analog test outputs

FB 250 ... FB 255

──────────────────────────────────────────────────────────────────

## 2.4.	Data Blocks

Data blocks (DB,DX) must not be loaded into an Eprom  module unless otherwise noted!
All data blocks except those in the Eprom will be generated automatically after a cold restart.

══════════════════════════════════════════════════════════════════

System Data Blocks

DB 0; DB 1; DX 0	DB 0	block address list

DB 1	periphery allocation

DX 0	system parameters3

──────────────────────────────────────────────────────────────────

User Data Blocks

General functions	DB 10	test

DB 10 ... DB 49	DB 11	time
		DB 12	flag memory

DB 21	PCU

-------------------------------------------------------------

Positions	DB 50	Positions

DB 50 ... DB 99	DB 51	requ'd by FB130

DB 99	requ'd by FB52

-------------------------------------------------------------

Drives and Operation	DB 150	drive data general / Az

DB 100   ...  DB 199	DB 151	drive system default parameters

DB 160	drive data GD

DB 170	drive data CH

DB 180	control loop standard parameters3

DB 181	control loop parameters Az

DB 182	control loop parameters GD

DB 183	control loop parameters CH

DB 184	control loop parameters bending

DB 189	control loop auxiliary DB

-------------------------------------------------------------

Interfaces	DB 221	data for CP581

DB 220 ... DB 239	DB 222	data from CP581

DB 223	program track data

DB 224	program track aux. DB

-------------------------------------------------------------

Monitoring	DB 250	analog test outputs

DB 240 ... DB 255

──────────────────────────────────────────────────────────────────

# Footnotes

no listing available

do not modify!

to be loaded into EPROM