To: file LCUSETUP
From: Jon Hagen
Date: 6-17-03
Subject: Bios for CP581 Pentium (silicon disk still w/o files)
Reference: Section 3.8 of Siemens Simatic CP581 User Manual

MAIN
F2 to enter setup
System time	HH MM SS (space bar increments; “+” key decrements!)
System date	MM DD YY
Legacy Diskette A:	[1.4MB/1.25MB 3 1/2"]
Legacy Diskette B:	Disabled
>Primary Master*	[8455 MB]
>Primary Slave*	[None]
>Keyboard Features*
Boot Sequence	[A: then C: ]
System Memory:	640 kB
Extended memory:	31744 k

Main Submenus
Primary Master Mode: [Auto] (“+” key toggles this through “Auto”, “User”, and “None”.)
“Auto” yields 17475 cylinders, 15 yeads, 63 sectors, max capacity 8455 MB, LBA mode control enabled.
Primary Slave Mode: [Auto] yields LBA mode control enabled.
Keyboard Features Numblock: [Auto] (“+” key toggles)

S5 INTERFACE
S5 Interface	[Disabled]
Page-Frames:	[Enabled}
Frames:	[4]
Mode:	[Paged]
Page Number:	[0]
Base: [??00h]	[244]
I/O-Pointer	[Disabled]
Range:	[P-PERIPHERIE]
Base: (FX..)	[0]
Pointer Read [Disabled]
>S5 Communications Flags*

S5 Interface Submenu
S5 Communication Flags (all set to “Disabled”)